## Slide 1
MGEQ1C064 Driver User Guide Serial Port 0 (UART0) MGEQ1C064_UART0_DRV.c
MGEQ1C064_UART0_DRV.h Version : v1.00

## Slide 2: Serial Port 0 Driver Macro List

## Slide 3
Macro Name | Macro Brief
__DRV_URT0_IT_Cmd(__STATE__) | Interrupt.
__DRV_URT0_DataOrder_Select(__ORDER__) | Data order.
__DRV_URT0_TimerMode_Select(__MODE__) | S0BRG timer mode.
__DRV_URT0_BaudRateX2_Select(__TIME__) | Enhance baud rate.
__DRV_URT0_BaudRateGeneratorClock_Select(__SOURCE__) | S0BRG clock source.
__DRV_URT0_S0Control_Cmd(__STATE__) | S0CR1 access enable.
__DRV_URT0_RXClockSource_Select(__SOURCE__) | Receive clock.
__DRV_URT0_TXClockSource_Select(__SOURCE__) | Transmit clock.
__DRV_URT0_BaudRateGenerator_Cmd(__STATE__) | S0BRG operation.
__DRV_URT0_BaudRateReloadReg_Write(__RELOAD__) | Baud rate generator reload register.
__DRV_URT0_SerialReception_Cmd(__STATE__) | Reception enable/disable.
__DRV_URT0_BaudRateDiv3_Cmd(__STATE__) | Mode 2 SYSCLK/32 or SYSCLK/64.
__DRV_URT0_Mode_Select(__MODE__) | Mode select.
__DRV_URT0_SetSM30(__MODE__) | Set SFR.

## Slide 4
Macro Name | Macro Brief
__DRV_URT0_SetSM00(__MODE__) | Set SFR.
__DRV_URT0_SetSM10(__MODE__) | Set SFR.
__DRV_URT0_PinMux_Select(__RXTX__) | Pin config.
__DRV_URT0_SetS0PS1(__RXTX__) | Set SFR.
__DRV_URT0_SetS0PS0(__RXTX__) | Set SFR.
__DRV_URT0_BaudRateX2X4_Select(__TIME__) | S0BRG enhance baud rate.
__DRV_URT0_SetSMOD2(__TIME__) | Set SFR.
__DRV_URT0_SetSMOD1(__TIME__) | Set SFR.
__DRV_URT01_S01MI_PinMux_Select(__RECEPTION__) | UART01 S01MI PinMux
__DRV_URT0_Block_S0IntFlag_Cmd(__STATE__) | Block TI0
__DRV_URT0_TI0toSYSINT_Cmd(__STATE__) | TI0 to system flag interrupt
__DRV_URT0_Lin_Bus_TxRx_Select(__RXTX__) | Lin TxRx
__DRV_URT0_Lin_Bus_BreakLength_Select(__LENGTH__) | Lin break length
__DRV_URT0_BaudRateSysclkDiv4_Cmd(__STATE__) | Mode 4 SYSCLK/4,SYSCLK/12

## Slide 5
Macro Name | Macro Brief
__DRV_URT0_Clock_Source_S1BRG_Select(__SOURCE__) | Clock source S1BRG select
__DRV_URT0_Baud_Rate_Generator_Clock_Output_Cmd(__STATE__) | Enable S0BRG clock output control
__DRV_URT0_BaudRateReloadReg16Bit_Write(__RELOAD__) | In mode2 pure timer 16 bit reload
__DRV_URT0_Pure_Timer_Baudrate_Generator_Overflow_to_S0_Interrupt_Cmd(__STATE__) | In mode 2 enable pure timer baudrate generator overflow to S0 interrupt
__DRV_URT0_Pure_Timer_External_Pin_Trigger_to_S0_Interrupt_Cmd(__STATE__) | In mode 2 enable pure timer external pin trigger to S0 interrupt
__DRV_URT0_Pure_Timer_External_Pin_Control_Baudrate_Generator_Cmd(__STATE__) | In mode 2 enable pure timer external pin control baudrate generator
__DRV_URT0_Pure_Timer_External_Pin_Trigger_Level_Cmd(__STATE__) | In mode 2 enable pure timer external pin trigger level
__DRV_URT0_Clock_Source_S0BRG_Select(__SOURCE__) | Clock source S0BRG select
__DRV_URT0_S0Control_Cmd(MW_ENABLE) | Set SFR
__DRV_URT0_SetS0TCK(__SOURCE__) | Set SFR
__DRV_URT0_SetS0RCK(__SOURCE__) | Set SFR
__DRV_URT0_Clock_Source_Timer2_Select(__SOURCE__) | Clock source timer2 select
_DRV_TIMER2_Function_Access_Control_Cmd(MW_DISABLE) | Set SFR
__DRV_URT0_SetTCLK(__SOURCE__) | Set SFR

## Slide 6
Macro Name | Macro Brief
__DRV_URT0_SetRCLK(__SOURCE__) | Set SFR
__DRV_URT0_Pure_Timer_Clock_Source_Select(__SOURCE__) | In mode2 pure timer clock source select
__DRV_URT0_SetS0TX12(__SOURCE__) | Set SFR
__DRV_URT0_SetSM20(__SOURCE__) | Set SFR

## Slide 7
Function Name | Function Brief
DRV_URT0_GetTI0() | Read TX interrupt flag.
DRV_URT0_GetRI0() | Read RX interrupt flag.
DRV_URT0_ClearTI0() | Clear TX interrupt flag.
DRV_URT0_ClearRI0() | Clear RX interrupt flag.
DRV_URT0_ClearSM20() | Disable SM20 function.
DRV_URT0_SetSM20() | Enable SM20 function.
DRV_URT0_SetSADDR(uint8_t Address) | Set SADDR .
DRV_URT0_SetSADEN(uint8_t Address ) | Set SADEN(Mask) .
DRV_URT0_SetTXData9th() | Transfer data.
DRV_URT0_ClearTXData9th() | Transfer data.
DRV_URT0_GetRXData9th() | Receive data.
DRV_URT0_SendTXData(uint8_t TXData) | Transfer data.
DRV_URT0_ReceiveRXData() | Receive data.
DRV_URT0_GetTransmitErrorFlag() | Lin get transmit-error-flag.

## Slide 8
Function Name | Function Brief
DRV_URT0_SetSyncBreakFlag() | Lin set sync-break-flag.
DRV_URT0_GetSyncBreakFlag() | Lin get sync-break-flag.
DRV_URT0_SetSyncBreak() | Lin set sync-break.
DRV_URT0_GetSyncBreak() | Lin get sync-break.
DRV_URT0_SetAutoBaudRate() | Lin SetAutoBaudRate.
DRV_URT0_SetTransmitErrorFlag() | Lin transmit-error-flag.
DRV_URT0_GetBaudRate() | Get baud rate.

## Slide 9: Serial Port 0 Driver Macro Introduction

## Slide 10
__DRV_URT0_Mode_Select(__MODE__)
__DRV_URT0_SetSM30(__MODE__)
__DRV_URT0_SetSM00(__MODE__)
__DRV_URT0_SetSM10(__MODE__)
Selection:
Shift Mode
8bit Mode
9bit Mode(SYSCLK/n)
9bit Mode(variable)
SPI Master Mode
LIN Mode
Example:
1. __DRV_URT0_Mode_Select(UART0_MODE0_SHIFT_REG)
2. __DRV_URT0_Mode_Select(UART0_MODE1_8BIT)
3. __DRV_URT0_Mode_Select(UART0_MODE2_9BIT)
4. __DRV_URT0_Mode_Select(UART0_MODE3_9BIT)
5. __DRV_URT0_Mode_Select(UART0_MODE4_SPI_MASTER)
6. __DRV_URT0_Mode_Select(UART0_MODE5_LIN)

## Slide 11
__DRV_URT0_Clock_Source_S0BRG_Select(__SOURCE__)
__DRV_URT0_SetS0TCK(__SOURCE__)
__DRV_URT0_S0Control_Cmd(MW_ENABLE)
__DRV_URT0_SetS0RCK(__SOURCE__)
Source:
TX :
Timer or S1BRG
RX:
Timer or S1BRG
TX :
Timer or S1BRG
RX:
S0BRG
TX :
S0BRG
RX:
Timer or S1BRG
TX :
S0BRG
RX:
S0BRG
Example:
1.__DRV_URT0_Clock_Source_S0BRG_Select(TRANSMIT_CLOCK_SOURCE_TIMER_S1BRG_RECEIVE_CLOCK_SOURCE_TIMER_S1BRG)
2. __DRV_URT0_Clock_Source_S0BRG_Select(TRANSMIT_CLOCK_SOURCE_TIMER_S1BRG_RECEIVE_CLOCK_SOURCE_S0BRG)
3. __DRV_URT0_Clock_Source_S0BRG_Select(TRANSMIT_CLOCK_SOURCE_S0BRG_RECEIVE_CLOCK_SOURCE_TIMER_S1BRG)
4. __DRV_URT0_Clock_Source_S0BRG_Select(TRANSMIT_CLOCK_SOURCE_S0BRG_RECEIVE_CLOCK_SOURCE_S0BRG)

## Slide 12
__DRV_URT0_Clock_Source_Timer2_Select(__SOURCE__)
__DRV_URT0_SetTCLK(__SOURCE__)
_DRV_TIMER2_Function_Access_Control_Cmd(MW_DISABLE)
__DRV_URT0_SetRCLK(__SOURCE__)
Source:
TX :
Timer1 or S1BRG
RX:
Timer1 or S1BRG
TX :
Timer1 or S1BRG
RX:
Timer2
TX :
Timer2
RX:
Timer1 or S1BRG
TX :
Timer2
RX:
Timer2
Example:
1. __DRV_URT0_Clock_Source_Timer2_Select(TRANSMIT_CLOCK_SOURCE_TIMER1_S1BRG_RECEIVE_CLOCK_SOURCE_TIMER1_S1BRG)
2. __DRV_URT0_Clock_Source_Timer2_Select(TRANSMIT_CLOCK_SOURCE_TIMER1_S1BRG_RECEIVE_CLOCK_SOURCE_TIMER2)
3. __DRV_URT0_Clock_Source_Timer2_Select(TRANSMIT_CLOCK_SOURCE_TIMER2_RECEIVE_CLOCK_SOURCE_TIMER1_S1BRG)
4. __DRV_URT0_Clock_Source_Timer2_Select(TRANSMIT_CLOCK_SOURCE_TIMER2_RECEIVE_CLOCK_SOURCE_TIMER2)

## Slide 13
__DRV_URT0_Pure_Timer_Clock_Source_Select(__SOURCE__)
__DRV_URT0_SetS0TX12(__SOURCE__)
__DRV_URT0_SetSM20(__SOURCE__)
Source:
SYSCLK/12
T1OF
SYSCLK/1
T0OF
Example:
1. __DRV_URT0_Pure_Timer_Clock_Source_Select(PURE_TIMER_CLOCK_SOURCE_SYSCLK_DIV_12)
2. __DRV_URT0_Pure_Timer_Clock_Source_Select(PURE_TIMER_CLOCK_SOURCE_T1OF)
3. __DRV_URT0_Pure_Timer_Clock_Source_Select(PURE_TIMER_CLOCK_SOURCE_SYSCLK_DIV_1)
4. __DRV_URT0_Pure_Timer_Clock_Source_Select(PURE_TIMER_CLOCK_SOURCE_T0OF)

## Slide 14
__DRV_URT0_PinMux_Select(__RXTX__)
__DRV_URT0_SetS0PS1(__RXTX__)
__DRV_URT0_SetS0PS0(__RXTX__)
Selection:
RX TX
P30 P31
P44 P45
P31 P30
P17 P22
Example:
1. __DRV_URT0_PinMux_Select(UART0_RX_P30_TX_P31)
2. __DRV_URT0_PinMux_Select(UART0_RX_P44_TX_P45)
3. __DRV_URT0_PinMux_Select(UART0_RX_P31_TX_P30)
4. __DRV_URT0_PinMux_Select(UART0_RX_P17_TX_P22)

## Slide 15
__DRV_URT0_BaudRateX2X4_Select(__TIME__)
__DRV_URT0_SetSMOD2(__TIME__)
__DRV_URT0_SetSMOD1(__TIME__)
Example:
1. __DRV_URT0_BaudRateX2X4_Select(UART0_DEFAULT_BAUD_RATE)
2. __DRV_URT0_BaudRateX2X4_Select(UART0_DOUBLE_BAUD_RATE_X1)
3. __DRV_URT0_BaudRateX2X4_Select(UART0_DOUBLE_BAUD_RATE_X2)
4. __DRV_URT0_BaudRateX2X4_Select(UART0_DOUBLE_BAUD_RATE_X4)
Selection:
Default baud rate
Double baud rate X1
Double baud rate X2
Double baud rate X4

## Slide 16
__DRV_URT0_IT_Cmd(__STATE__)
Cmd:
DISABLE
ENABLE
Example:
1. __DRV_URT0_IT_Cmd(MW_DISABLE)
2. __DRV_URT0_IT_Cmd(MW_ENABLE)
__DRV_URT0_DataOrder_Select(__ORDER__)
Selection:
Data order
Example:
1. __DRV_URT0_DataOrder_Select(UART0_DATA_ORDER_LSB)
2. __DRV_URT0_DataOrder_Select(UART0_DATA_ORDER_MSB)

## Slide 17
__DRV_URT0_TimerMode_Select(__MODE__)
Selection :
8/16 bit timer mode
Example:
1. __DRV_URT0_TimerMode_Select(S0BRG_8BIT_TIMER_MODE)
2. __DRV_URT0_TimerMode_Select(S0BRG_16BIT_TIMER_MODE)
__DRV_URT0_BaudRateX2_Select(__TIME__)
Selection:
Default baud rate
Double baud rate X1
Example:
1. __DRV_URT0_BaudRateX2_Select(UART0_DEFAULT_BAUD_RATE)
2. __DRV_URT0_BaudRateX2_Select(UART0_DOUBLE_BAUD_RATE_X1)

## Slide 18
__DRV_URT0_BaudRateGeneratorClock_Select(__SOURCE__)
Selection :
SYSCLK/1
SYSCLK/12
Example:
1. __DRV_URT0_BaudRateGeneratorClock_Select(S0BRG_CLOCK_SOURCE_SYSCLK_DIV_1)
2. __DRV_URT0_BaudRateGeneratorClock_Select(S0BRG_CLOCK_SOURCE_SYSCLK_DIV_12)
__DRV_URT0_S0Control_Cmd(__STATE__)
Cmd:
Disable
Enable
Example:
1. __DRV_URT0_S0Control_Cmd(MW_ENABLE)
2. __DRV_URT0_S0Control_Cmd(MW_DISABLE)

## Slide 19
__DRV_URT0_RXClockSource_Select(__SOURCE__)
Selection :
Receive Clock S0BRG
Receive Clock Timer or S1BRG
Example:
1. __DRV_URT0_RXClockSource_Select(RECEIVE_CLOCK_S0BRG)
2. __DRV_URT0_RXClockSource_Select(RECEIVE_CLOCK_SYSCLK_TIMER_S1BRG)
__DRV_URT0_TXClockSource_Select(__SOURCE__)
Selection:
Transmit Clock S0BRG
Transmit Clock Timer or S1BRG
Example:
1. __DRV_URT0_TXClockSource_Select(TRANSMIT_CLOCK_S0BRG)
2. __DRV_URT0_TXClockSource_Select(TRANSMIT_CLOCK_SYSCLK_TIMER_S1BRG)

## Slide 20
__DRV_URT0_BaudRateGenerator_Cmd(__STATE__)
Cmd :
Disable
Enable
Example:
1. __DRV_URT0_BaudRateGenerator_Cmd(MW_ENABLE)
2. __DRV_URT0_BaudRateGenerator_Cmd(MW_DISABLE)
__DRV_URT0_BaudRateReloadReg_Write(__RELOAD__)
Write:
Baud Rate Generator Reload
Example:
1. __DRV_URT0_BaudRateReloadReg_Write(S0BRG_BRGRL_2400_1X_12000000_12T)
2. __DRV_URT0_BaudRateReloadReg_Write(S0BRG_BRGRL_4800_1X_12000000_12T)

## Slide 21
__DRV_URT0_SerialReception_Cmd(__STATE__)
Cmd:
Disable
Enable
Example:
1. __DRV_URT0_SerialReception_Cmd(MW_ENABLE)
2. __DRV_URT0_SerialReception_Cmd(MW_DISABLE)
__DRV_URT0_BaudRateDiv3_Cmd(__STATE__)
Cmd:
Disable
Example:
1. __DRV_URT0_BaudRateDiv3_Cmd(MW_DISABLE)

## Slide 22
Cmd:
Disable
Enable
Example:
1. __DRV_URT0_BaudRateSysclkDiv4_Cmd(MW_ENABLE)
2. __DRV_URT0_BaudRateSysclkDiv4_Cmd((MW_DISABLE)
__DRV_URT0_BaudRateSysclkDiv4_Cmd(__STATE__)
__DRV_URT0_Block_S0IntFlag_Cmd(__STATE__)
Cmd:
Disable
Enable
Example:
1. __DRV_URT0_Block_S0IntFlag_Cmd(MW_ENABLE)
2. __DRV_URT0_Block_S0IntFlag_Cmd(MW_DISABLE)

## Slide 23
__DRV_URT0_TI0toSYSINT_Cmd(__STATE__)
Cmd:
Disable
Enable
Example:
1. __DRV_URT0_Block_S0IntFlag_Cmd(MW_ENABLE)
2. __DRV_URT0_Block_S0IntFlag_Cmd(MW_DISABLE)
__DRV_URT01_S01MI_PinMux_Select(__RECEPTION__)
Selection:
S01MI Pin MUX
Example:
1. __DRV_URT01_S01MI_PinMux_Select(UART0_S0MI_P16_UART1_S1MI_P61)
2. __DRV_URT01_S01MI_PinMux_Select(UART0_S0MI_P33_UART1_S1MI_P47)

## Slide 24
__DRV_URT0_Lin_Bus_TxRx_Select(__RXTX__)
Selection:
Lin TxRx
Example:
1. __DRV_URT0_Lin_Bus_TxRx_Select(UART0_LIN_BUS_RX)
2. __DRV_URT0_Lin_Bus_TxRx_Select(UART0_LIN_BUS_TX)
__DRV_URT0_Lin_Bus_BreakLength_Select(__LENGTH__)
Selection:
Lin Break Length Select
Example:
1.__DRV_URT0_Lin_Bus_BreakLength_Select(UART0_LIN_BUS_BREAK13)
2.__DRV_URT0_Lin_Bus_BreakLength_Select(UART0_LIN_BUS_BREAK16)

## Slide 25
__DRV_URT0_Clock_Source_S1BRG_Select(__SOURCE__)
Selection:
Clock Source
S1BRG Select
Example:
1.__DRV_URT0_Clock_Source_S1BRG_Select(TRANSMIT_CLOCK_SOURCE_TIMER1_RECEIVE_CLOCK_SOURCE_TIMER1)
2.__DRV_URT0_Clock_Source_S1BRG_Select(TRANSMIT_CLOCK_SOURCE_S1BRG_RECEIVE_CLOCK_SOURCE_S1BRG)
S0BRG Clock Output (S0BRG in 8-bit Timer Mode)

## Slide 26
__DRV_URT0_Baud_Rate_Generator_Clock_Output_Cmd(__STATE__)
Cmd:
Disable
Enable
Example:
1.__DRV_URT0_Baud_Rate_Generator_Clock_Output_Cmd(MW_DISABLE)
2.__DRV_URT0_Baud_Rate_Generator_Clock_Output_Cmd(MW_ENABLE)
S0BRG Clock Output (S0BRG in 8-bit Timer Mode)

## Slide 27
__DRV_URT0_BaudRateReloadReg16Bit_Write(__RELOAD__)
Write:
Mode2 Pure Timer
16 Bit Reload
Example:
1. __DRV_URT0_BaudRateReloadReg16Bit_Write(0)
2. __DRV_URT0_BaudRateReloadReg16Bit_Write(65535)

## Slide 28
__DRV_URT0_Pure_Timer_Baudrate_Generator_Overflow_to_S0_Interrupt_Cmd(__STATE__)
Cmd:
Disable
Enable
Example:
1.__DRV_URT0_Pure_Timer_Baudrate_Generator_Overflow_to_S0_Interrupt_Cmd(MW_DISABLE)
2.__DRV_URT0_Pure_Timer_Baudrate_Generator_Overflow_to_S0_Interrupt_Cmd(MW_ENABLE)

## Slide 29
__DRV_URT0_Pure_Timer_External_Pin_Trigger_to_S0_Interrupt_Cmd(__STATE__)
Cmd:
Disable
Enable
Example:
1. __DRV_URT0_Pure_Timer_External_Pin_Trigger_to_S0_Interrupt_Cmd(MW_DISABLE)
2. __DRV_URT0_Pure_Timer_External_Pin_Trigger_to_S0_Interrupt_Cmd(MW_ENABLE)

## Slide 30
__DRV_URT0_Pure_Timer_External_Pin_Control_Baudrate_Generator_Cmd(__STATE__)
Cmd:
Disable
Enable
Example:
1. __DRV_URT0_Pure_Timer_External_Pin_Control_Baudrate_Generator_Cmd(MW_DISABLE)
2. __DRV_URT0_Pure_Timer_External_Pin_Control_Baudrate_Generator_Cmd(MW_ENABLE)

## Slide 31
__DRV_URT0_Pure_Timer_External_Pin_Trigger_Level_Cmd(__STATE__)
Cmd:
Disable
Enable
Example:
1. __DRV_URT0_Pure_Timer_External_Pin_Trigger_Level_Cmd(MW_DISABLE)
2. __DRV_URT0_Pure_Timer_External_Pin_Trigger_Level_Cmd(MW_ENABLE)

## Slide 32
DRV_URT0_GetTI0()
Get:
Read TX Interrupt Flag
Example:
if(DRV_URT0_GetTI0())
{
…………………………………….
}
DRV_URT0_GetRI0()
Get:
Read RX Interrupt Flag
Example:
if(DRV_URT0_GetRI0())
{
…………………………………….
}

## Slide 33
DRV_URT0_ClearTI0()
Clear:
Clear TX Interrupt Flag
Example:
DRV_URT0_ClearTI0()
DRV_URT0_ClearRI0()
Clear:
Clear RX Interrupt Flag
Example:
DRV_URT0_ClearRI0()

## Slide 34
DRV_URT0_ClearSM20()
Clear:
Disable SM20 Function
Example:
DRV_URT0_ClearSM20()
DRV_URT0_SetSM20()
Set:
Automatic Address
Recognition Feature
in Modes 2 and 3
Example:
DRV_URT0_SetSM20()
Note:
(1) After address matching (addr_match=1), Clear SM20 to receive data bytes
(2) After all data bytes have been received, Set SM20 to wait for next address.

## Slide 35
DRV_URT0_SetSADDR(uint8_t Address )
Set:
Set Address 0~255
Example:
DRV_URT0_SetSADDR(0)
DRV_URT0_SetSADEN(uint8_t Address )
Set:
Set SADEN 0~255
Example:
DRV_URT0_SetSADEN(0)
Slave 0 SADDR = 1100 0000 SADEN = 1111 1101 Given = 1100 00X0 | Slave 1 SADDR = 1100 0000 SADEN = 1111 1110 Given = 1100 000X
In the above example SADDR is the same and the SADEN data is used to differentiate between the two slaves.
In the above example the differentiation among the 3 slaves
Slave 0 SADDR = 1100 0000 SADEN = 1111 1001 Given = 1100 0XX0 | Slave 1 SADDR = 1110 0000 SADEN = 1111 1010 Given = 1110 0X0X | Slave 2 SADDR = 1110 0000 SADEN = 1111 1100 Given = 1110 00XX

## Slide 36
DRV_URT0_SetTXData9th()
Set:
Transfer 9th bit
Example:
DRV_URT0_SetTXData9th()
DRV_URT0_ClearTXData9th()
Clear:
Transfer 9th bit
Example:
DRV_URT0_ClearTXData9th()

## Slide 37
DRV_URT0_GetRXData9th()
Get:
Receive 9th bit
Example:
Temp=DRV_URT0_GetRXData9th()
DRV_URT0_SendTXData(uint8_t TXData)
Send:
Transfer Data(byte)
Example:
DRV_URT0_SendTXData(255)

## Slide 38
DRV_URT0_ReceiveRXData()
Receive:
Receive Data(byte)
Example:
Temp=DRV_URT0_ReceiveRXData()
DRV_URT0_SetSyncBreakFlag()
Set:
Lin Set Sync-Break-Flag
Example:
DRV_URT0_SetSyncBreakFlag()

## Slide 39
DRV_URT0_GetSyncBreakFlag()
Get:
Lin Read Sync-Break-Flag
Example:
If(DRV_URT0_GetSyncBreakFlag())
{
………………………..
}
DRV_URT0_SetSyncBreak()
Set:
Lin sync-break(SYNC0).
If set in master mode,
next writing S0BUF will send a Sync-Break on LIN bus.
If set in slave mode,
the LIN interface engine will wait to receive a Sync-Break
and Auto cleared when Sync-Break is sent or received .
Example:
DRV_URT0_SetSyncBreakFlag()

## Slide 40
DRV_URT0_GetSyncBreak()
Get:
Lin Read Sync-Break(SYNC0)
Example:
If(DRV_URT0_GetSyncBreak())
{
………………………..
}
DRV_URT0_SetAutoBaudRate()
Set:
Lin Auto Baud Rate(ATBR0)
Example:
DRV_URT0_SetAutoBaudRate()

## Slide 41
DRV_URT0_GetBaudRate()
Get:
Get Baud Rate
Example: T
Temp=DRV_URT0_GetBaudRate()
DRV_URT0_SetTransmitErrorFlag()
Set:
Lin Transmit-Error-Flag
Example:
DRV_URT0_SetAutoBaudRate()

## Slide 42
DRV_URT0_GetTransmitErrorFlag()
Get:
Lin Transmit-Error-Flag
Example:
If(DRV_URT0_GetTransmitErrorFlag())
{
…………………………
}

## Slide 43
The End
Thank you !!!